## Slide 1
Reuniões Semanais #6 PC2023:0001:V3
ATA
Alencar Tecnologia da Amazonia.
CNPJ: 45.845.459/0001-24

## Slide 2: Agenda
Hardware Overview;
Components Description;
Power Consumption;
Data Sampling;
Application;
ATA
Alencar Tecnologia da Amazonia
CNPJ: 45.845.459/0001-24

## Slide 3: Hardware Overview
ATA
Alencar Tecnologia da Amazonia
CNPJ: 45.845.459/0001-24
Custom Board
Controller:
  ESP32 WROOM (BLE v4.0 & Wifi 802.11 b/g)
  Embedded RTC
  Firmware Micropython 1.20
Storage:
  micro SD Card Slot
Sensors:
  4x1 I2C Temperature, Humidity, Air Pressure and Air Quality
  Mic I2S
  LDR 5mm (ADC)

## Slide 4: Hardware Overview
ATA
Alencar Tecnologia da Amazonia
CNPJ: 45.845.459/0001-24
Custom Board
Dimensions:
  60mm x 50mm x 20mm
Other characteristics:
  4x Holes for board supporting: 5mm
  1x Led RGB THP
  2x Pushbuttons: Reset / Boot (firmware writing or regular button)
  USB Breakout Pads
  Voltage Regulator AP2112K-TGR-3.3v
  Exposed UART vias

## Slide 5: Components Descriptions
ATA
Alencar Tecnologia da Amazonia
CNPJ: 45.845.459/0001-24
Component | Value
USB Power Supply (Module) | ~ 0.40
Voltage Regulator (AP2112) | ~ 0.10
LDR (Photoresistor) 5mm | ~ 0.01
Led RGB THP 5mm | ~ 0.02
MicroSD Module | ~ 0.25
I2S Mic | ~ 1.80
BME680 4x1 Sensor | ~ 3.70
ESP32-WROOM-32 | ~ 3.50
PCB | ~ 5.00
PowerBank (50A) | ~ 20.00
Waterproof Box – IP67 – 20x12x7.5cm | ~ 10.00
ESTIMATED COST | ~ 44,78

## Slide 6: Power Consumption
Power Supply:
APK2112: 2.8V ~ 6.5V @ 800A - 3.3V @ 600mA
Operation mode:
Reading Sensors: 50mA
SD Writing: 70mA
Deepsleep: 15mA
Waking up: 100mA
BLE: 170mA (TX) ~ 200mA (RX)
ATA
Alencar Tecnologia da Amazonia
CNPJ: 45.845.459/0001-24

## Slide 7: Power Consumption
Consumption Estimation:
Routine: 1 min recording, 5 min sleeping;
Cycle: Sleep (5min), Wakeup (2s), Record (1min), Writing (2s)
Repetat the cycle for 1 hour (~ 10 cycles / hour)
ATA
Alencar Tecnologia da Amazonia
CNPJ: 45.845.459/0001-24
Current (mA/h) | Activity (duration/hour)
12,5 | Sleeping (~50 min/hour)
0,555556 | Waking Up (~20sec/hour)
8,333333 | Recording (~10min/hour)
0,388889 | Writing (~20sec/hour)
21,77778 | Routine Consumption (mAh)
Estimation 30mAh (3.3V - 0.15 Wh) | 

## Slide 8: Data sampling
ATA
Alencar Tecnologia da Amazonia
CNPJ: 45.845.459/0001-24
Chart: Temperature (ºC)
Chart: Humidity (%)
Chart: Atmospheric Pressure (Pa)
Chart: Air Quality Index (AQI Verage)
Chart: Luminosity (%)

## Slide 9: Data sampling
ATA
Alencar Tecnologia da Amazonia
CNPJ: 45.845.459/0001-24
Audio Samples:
File name: record_N.wav
Format: WAV
Storage Consumption: 2.55MB/min
Audio splited in 1 min chunks

## Slide 10: Application
Bluetooth Low Energy Configuration
  Real time data (Sensor Readings)
  Date Time / GPS Coordinates Sync
  Scheduling Management
Activity Scheduling
  Days of Week
  Start Time
  Start Date
  Recording Interval: 0 (disabled) ~ 24h
  Multiple Scheduling
ATA
Alencar Tecnologia da Amazonia
CNPJ: 45.845.459/0001-24

## Slide 11
Obrigado!
PC2023:0001:V3
ATA
Alencar Tecnologia da Amazonia.
CNPJ: 45.845.459/0001-24